What is this for?
Algorithm overview
use local time clock to
decode the timing key of source node
verify security of packet
use different time values for subsequent transmissions.

Nodes must be statically deployed.
Message sizes are fixed.
Each message includes the ID and local counter of the sender.
Keys are a function of the current time and the initialization vector (IV)

Each node has a tick window that contains a spread of time offsets.
The window is computed using variables consisting of:
a) The processing time it takes to create the messages
b) The possible time drift
c) Propagation delay

Time-Based Key Management (TKM)
creating of keys that will be used by crypto dynamically using local time.
Crypto (CRYPT)
addresses the security part of the problem
Obtains time-based keys from the TKM and attempts to decrypt incoming message.
The smaller the window, the less keys will be used and the faster the algorithm is.
Process continues until the correct key is found or the message is marked as malicious.
Uses RC4 encryption algorithm.

Filtering-Forwarding (FFWD)
filters incoming malicious packet or forwards packet

Steps
1) Source nodes are synchronized and loaded with a network-wide initialization vector (IV) pre-deployment.
1a) IV + local time will be used to generate dynamic keys

Benefits
vs. en-route-filtering scheme
keys being refreshed and distributed cost energy
not “chatty”, helps with radio silence.

Non-benefits
Only consider false inject and eavesdropping of messages. Insider attacks not considered.

results
significantly less energy consumption then at least five other en-route filtering protocols.
Energy consumption remains constant in the event of an attack.
Key trails increase linearly with an increase of malicious nodes.

Outline
T = TICK
A = APEC
[X] = Link

1) Describe previous attempts at:
a) Authentication
b) Encryption

2) Our Motivation

3) Brief Discussion
a) APEC
b) TICK

4) Merger (ideas)

5) Simulation (Technologies)