Definitions

8PSK: Phase-shift keying (PSK) is a digital modulation scheme that conveys data by changing (modulating) the phase of a reference signal (the carrier wave). The modulation is impressed by varying the sine and cosine inputs at a precise time. It is widely used for wireless LANs, RFID and Bluetooth communication.

CBP: A contention-based protocol (CBP) is a communications protocol for operating wireless telecommunication equipment that allows many users to use the same radio channel without pre-coordination. The "listen before talk" operating procedure in IEEE 802.11 is the most well known contention-based protocol.

CSMA: Carrier sense multiple access (CSMA) is a probabilistic media access control (MAC) protocol in which a node verifies the absence of other traffic before transmitting on a shared transmission medium, such as an electrical bus, or a band of the electromagnetic spectrum. Carrier sense means that a transmitter attempts to determine whether another transmission is in progress before initiating a transmission. That is, it tries to detect the presence of a carrier signal from another node before attempting to transmit. If a carrier is sensed, the node waits for the transmission in progress to end before initiating its own transmission. In other words, CSMA is based on the principle "sense before transmit" or "listen before talk".

DSSS: direct-sequence spread spectrum (DSSS) is a spread spectrum modulation technique. Spread spectrum systems are such that they transmit the message bearing signals using a bandwidth that is in excess of the bandwidth that is actually needed by the message signal. This spreading of the transmitted signal over a large bandwidth make the resulting wideband signal appear as a noise signal which allows greater resistance to intentional and unintentional interference with the transmitted signal.[1]

EGPRS: Enhanced General Packet Radio Service (GPRS) is a packet oriented mobile data service on the 2G and 3G cellular communication system's global system for mobile communications (GSM). GPRS was originally standardized by European Telecommunications Standards Institute (ETSI) in response to the earlier CDPD and i-mode packet-switched cellular technologies. It is now maintained by the 3rd Generation Partnership Project (3GPP).[1][2]

FBMC: Filter bank multicarrier.

FDM: frequency-division multiplexing (FDM) is a technique by which the total bandwidth available in a communication medium is divided into a series of non-overlapping frequency sub-bands, each of which is used to carry a separate signal. This allows a single transmission medium such as the radio spectrum, a cable or optical fiber to be shared by multiple independent signals. Another use is to carry separate serial bits or segments of a higher rate signal in parallel.

GMSK: In digital communication, Gaussian minimum shift keying or GMSK is a continuous-phase frequency-shift keying modulation scheme. GMSK is similar to standard minimum-shift keying (MSK); however the digital data stream is first shaped with a Gaussian filter before being applied to a frequency modulator, and typically has much narrower phase shift angles than most MSK modulation systems. This has the advantage of reducing sideband power, which in turn reduces out-of-band interference between signal carriers in adjacent frequency channels.

GSM: (Global System for Mobile Communications, originally Groupe SpécialMobile), is a standard developed by the European Telecommunications Standards Institute (ETSI) to describe the protocols for second-generation (2G) digital cellular networks used by mobile phones, first deployed in Finland in July 1991.[2] As of 2014it has become the de facto global standard for mobile communications - with over 90% market share, operating in over 219 countries and territories

MANET: A mobile ad hoc network (MANET) is a continuously self-configuring, infrastructure-less network of mobile devices connected wirelessly.[1] Each device in a MANET is free to move independently in any direction, and will therefore change its links to other devices frequently. Each must forward traffic unrelated to its own use, and therefore be arouter. The primary challenge in building a MANET is equipping each device to continuously maintain the information required to properly route traffic[1]. Such networks may operate by themselves or may be connected to the larger Internet. They may contain one or multiple and different transceivers between nodes. This results in a highly dynamic, autonomous topology.[2]

OFDM: Orthogonal frequency-division multiplexing (OFDM) is a method of encoding digital data on multiple carrier frequencies. OFDM has developed into a popular scheme for wideband digital communication, used in applications such as digital television and audio broadcasting, DSL Internet access, wireless networks,powerline networks, and 4G mobile communications.

SAIC: Single antenna interference cancellation (SAIC) is a promising technology to boost the capacity of GSM networks without any needed change in the network.

SS: spread-spectrum techniques are methods by which a signal (e.g. an electrical, electromagnetic, or acoustic signal) generated with a particular bandwidth is deliberately spread in the frequency domain, resulting in a signal with a wider bandwidth. These techniques are used for a variety of reasons, including the establishment of secure communications, increasing resistance to natural interference, noise and jamming, to prevent detection, and to limit power flux density (e.g. in satellite downlinks).

TDMA: Time division multiple access (TDMA) is a channel access method for shared medium networks. It allows several users to share the same frequency channel by dividing the signal into different time slots.[1]The users transmit in rapid succession, one after the other, each using its own time slot. This allows multiple stations to share the same transmission medium (e.g. radio frequency channel) while using only a part of its channel capacity. TDMA is used in the digital 2G cellular systems such as Global System for Mobile Communications (GSM), IS-136, Personal Digital Cellular (PDC) and iDEN, and in the Digital Enhanced Cordless Telecommunications (DECT) standard for portable phones. It is also used extensively in satellite systems, combat-net radio systems, and PON networks for upstream traffic from premises to the operator. For usage of Dynamic TDMA packet mode communication, see below.

WSN: Wireless sensor networks (WSN), sometimes called wireless sensor and actuator networks (WSAN),[1][2] are spatially distributed autonomous sensors to monitor physical or environmental conditions, such as temperature, sound, pressure, etc. and to cooperatively pass their data through the network to a main location. The more modern networks are bi-directional, also enabling control of sensor activity. The development of wireless sensor networks was motivated by military applications such as battlefield surveillance; today such networks are used in many industrial and consumer applications, such as industrial process monitoring and control, machine health monitoring, and so on.